## Slide 1: Barrier Coverage with Optimized Quality for Wireless Sensor Networks
Yung-Liang Lai*, Jehn-Ruey Jiang
National Central University
Taoyuan Innovation Institute of Technology*
Taiwan

## Slide 2: Wireless Sensor based Barrier Coverage
USA
Wireless sensor
Notes: We can deploy some wireless sensors in a protected area
to detect the intruders.
The wireless sensors are

## Slide 3: Barrier Coverage Optimization Problem
How to construct a barrier coverage such that :
Degree of Detecting intruders is Maximized ,
Probability of Detecting intruders is Maximized Data transmission time is Minimized?
Notes: In this paper,
We model a barrier coverage optimization problem.
The problem is how to construct a barrier coverage such that degree ….

## Slide 4: Barrier Coverage Optimization Problem
To optimize Quality of Barrier Coverage
  We define three Quality metrics
    detection degree, detection probability, expected transmission time
  We model the problem as a Graph Problem
  Solve it by the Minimum Cost Maximum Flow Algorithm
Notes: In this paper, we study the barrier coverage optimization problem, which is used to optimize quality of barrier coverage
    We define three quality metrics : detection degree, detection probability, expected transmission time
    We model the problem as a graph problem
    And solve it by maximum flow minimum cost planning approach

## Slide 5: Outline
Background
Network Modeling
Barrier Coverage Optimization Problem
Optimal Barrier Coverage Algorithm
Time Complexity Analysis
Conclusion
Notes: This is the outline

## Slide 6: Background
  k-Barrier Coverage Problem
  Sink Connected Barrier Coverage
Notes: We introduce two definitions

## Slide 7: k-Barrier Coverage Problem
Degree (k) is the number of virtual detection lines
How to select nodes to maximize degree (k)
Given:
Solution: k=2
Notes: Degree (k) is the number of virtual detection lines
As shown in right, its degree is 2, which means the number of virtual detection lines is 2.
It means a intruder will be detected at least two times.
The k-Barrier Coverage problem is how to select nodes to maximize degree (k) in an given nodes set.

## Slide 8: Sink Connected Barrier Coverage
Intruder
Boundary area
Sensor node for only forwarding events
Sink Node
Sensor node (center dot) with a sensing area for detecting and forwarding events
Transmission Link
Detection Line
Notes: In our previous work, we define the sink connected barrier coverage, which is to construct a barrier coverage with connectivity to the sink nodes

## Slide 9: Outline
Background
Network Modeling
Barrier Coverage Optimization Problem
Optimal Barrier Coverage Algorithm
Time Complexity Analysis
Conclusion

## Slide 10: Network Model
Coverage Graph Gc
Transmission Graph Gt
Notes: To model our problem, we define two graphs : coverage graph and transmission graph

## Slide 11: Coverage Graph (Gc)
Ni and Nj have overlapped sensing coverage, then Edge (Ni, Nj) exists
Notes: In a coverage graph, if two nodes have overlapped coverage, then edge exists in coverage graph

## Slide 12: Coverage Graph (Gc)
Detection Probability
  depend on distance
  P(d)=e-d
Detection Quality
  Worst Case of P
  Pw(Si, Sj)=P( Dist / 2 )
sensor
target
S i
S j
Distance (d)
Intruder Path in Middle
(Worst Case)
P(d)
Dist
Notes: Now, we will define

## Slide 13: Transmission Graph (Quality)
<Ni, Nj> = node Ni can transmit data to Nj
Detection Quality

## Slide 14: Transmission Graph (Gt)
Weight of edge on Gt
  Quality of Link:
N5
N6
N7
N9
N11
N10
N12
N13
K2
K1
N4
N1
N2
N3
N14
1
3
2
2
2
3
1
1
2
4
2
2
2
N8
Packet size
Bandwidth
Successful Ratio of Sending Packet
Successful Ratio of ACK Packet

## Slide 15: Transmission Graph (Gt)
  Quality of Path Set:
    To measure the expected transmission time of a path set(PS)
N5
N6
N7
N9
N11
N10
N12
N13
K2
K1
N4
N1
N2
N3
N14
1
3
2
2
2
3
1
1
2
4
2
2
2
N8

## Slide 16: Outline
Background
Network Modeling
Barrier Coverage Optimization Problem
Optimal Barrier Coverage Algorithm
Time Complexity Analysis
Conclusion

## Slide 17: Barrier Coverage Optimization Problem
(k,p,t)–Barrier Coverage Optimization Problem
How to select nodes from randomly deployed sensor nodes to reach three goals :
  Goal 1: Maximizing the degree k of barrier coverage
  Goal 2: Maximizing the minimum probability p of detecting intruders crossing the monitoring region
  Goal 3: Minimizing the expected transmission time t to send data to the sink nodes.

## Slide 18: Outline
Background
Barrier Coverage Optimization Problem
Optimal Barrier Coverage Algorithm
Optimal Barrier Coverage Algorithm
  Backgroud: Maximum Flow Algorithm & Maximum Flow Minimum Algorithm
  Optimal Barrier Coverage Algorithm
Time Complexity Analysis
Conclusion

## Slide 19: Background: Maximum Flow Algorithm
Maximum Flow (MaxFlow) ALG
  Each edge is assigned capacity constraint
  To find some flows from s to t , such that:
    Number of Flow is Maximized
Flow on edge
capacity
Maximum Flow Plan = 2 Flows
Notes: Now, we introduce the maximum flow algorithm.
The maximum flow algorithm is to find some flows from s to t, such that number of flow is maximized under capacity constraints

## Slide 20: Background: Maximum Flow Algorithm
Maximum Flow (MaxFlow) ALG
  To find MaxFlow plan from s to t , such that:
    Number of Flow () is Maximized
2 Flows
Notes: In this example, the maximum number of flow is 2.

## Slide 21: Background: Maximum Flow Minimum Cost Algorithm
Maximum Flow Minimum Cost (MaxFlowMinCost) ALG
  To find flows from s to t , such that:
$2
$1
$3
$1
$2
$1
$1
$1
Flow value
capacity

## Slide 22: Background: Maximum Flow Minimum Cost Algorithm
Maximum Flow Minimum Cost (MaxFlowMinCost) ALG
  To find flows from s to t , such that:
    Number of Flow() is Maximized
    Total Cost ($) is Minimized
$2
$1
$3
$1
$2
$1
$1
$1
Flow value
capacity

## Slide 23: Optimal Barrier Coverage Algorithm
Basic Idea : 3 Phases
  Phase1)To find a set of nodes (FP) with maximized number of node-disjointed flows (k) in Coverage Graph (Gc) by MaxFlow ALG
  Phase2)To refine FP such that minimum detection probability (p) is maximized by MaxFlow ALG
  Phase3)To select some additional nodes for connecting sink nodes with minimized Expected Transmission Time (t) by MaxFlowMinCost ALG

## Slide 24: Phase1
  To find a set of nodes (FP) with maximized number of node-disjointed flows (k) in Coverage Graph (Gc) by MaxFlow ALG
K=2

## Slide 25: Phase 2
  (Repeatedly remove edges such that minimum detection probability (p) is Maximized without loss number of flows in Phase 1
N5
N6
N7
N3
N4
N2
N1
N9
N8
0.6
0.6
0.4
0.6
0.5
0.6
0.7
0.6
Minimum detection probability =0.4
N5
N6
N7
N3
N4
N2
N1
N9
N8
0.6
0.6
0.6
0.5
0.6
0.7
0.6
Minimum detection probability =0.5
Quality of Barrier Coverage = 0.4
Quality of Barrier Coverage = 0.5
X

## Slide 26: Phase 3
To select some additional nodes for connecting sink nodes with minimized Expected Transmission Time (t) by MaxFlowMinCost ALG
N5
N6
N7
N9
N11
N10
N12
N13
K2
K1
N4
N1
N2
N3
N14
1
3
2
2
2
3
1
1
2
4
2
2
2
N8
N5
N6
N7
N9
N11
N10
N12
N13
K2
K1
N4
N1
N2
N3
1
3
2
2
2
3
1
1
2
4
2
2
2
N8
(5)
(4)
(4)
(2)
(2)
(5)
(5)
(3)
Expected Transmission Time = (5+4+4+2 + 2+5+5+3)/8
, which is Optimized

## Slide 27: Optimal Barrier Coverage Algorithm
Step 1: Construct a coverage graph Gc
  Each edge is associated with a weight (detection probability)
N5
N6
N7
N3
N4
N2
N1
N9
N8
0.6
0.5
0.4
0.5
0.5
0.6
0.7
0.6

## Slide 28: Optimal Barrier Coverage Algorithm
For Multiple-in & Multiple-Out
Step 2: Execute to Node-Disjoint Transformation transfer Gc into the new graph Gc*
Node-Disjoint Transformation

## Slide 29: Optimal Barrier Coverage Algorithm
Step 3:(To Find Maximum barrier coverage)
  Execute the maximum flow algorithm on Gc* to decide the maximum flow plan FP
S
T
N5
N6
N7
N3
N4
N2
N1
N9
N8
0.6
0.5
0.4
0.5
0.5
0.6
0.7
0.6

## Slide 30: Optimal Barrier Coverage Algorithm
Step 4: Remove all edges with the minimal probability without loss of Degree(k)
  Can we remove the MIN edge without loss number of flows?
  Yes, remove it and continue to test
  No, quality is maximized
S
T
0.6
0.6
0.6
0.4
0.5

## Slide 31: Optimal Barrier Coverage Algorithm
Step 4: Remove all edges with the minimal probability without loss of Degree(k)
  Can we remove the MIN edge without loss number of flows?
  Yes, remove it and continue to test
  No, quality is maximized
S
T
0.6
0.6
0.6
0.4
0.5

## Slide 32: Optimal Barrier Coverage Algorithm
Step 4: Remove all edges with the minimal probability without loss of Degree(k)
  Can we remove the MIN edge without loss number of flows?
  Yes, remove it and continue to test
  No, quality is maximized
S
T
0.6
0.6
0.6
0.5
A Barrier is constructed with MIN_Quality=0.5

## Slide 33: Optimal Barrier Coverage Algorithm
Step 5: Construct a transmission graph
  Add a virtual source node S and a virtual target node T
T
S

## Slide 34: Optimal Barrier Coverage Algorithm
Step 6: For each node selected in Step. 4, add an edge from S, For each sink node, add edge to T
  The ETT (Expected Transmission Time) is assigned on each edge
T
S

## Slide 35: Optimal Barrier Coverage Algorithm
Step 7: Execute Maximum Flow Minimum Cost Algorithm
T
S
Maximum Flow with Minimized Cost
    Thus, a node set with maximized degree (k),
    maximized minimum_detection_probability (p), and
    minimized average transmission time (t) is determined

## Slide 36: Time Complexity Analysis
Time complexity of Optimal Barrier Coverage Algorithm is dominated by step 4
  Try to remove minimum weight edge on coverage graph and to execute maximum flow algorithm, repeatedly (in step 4)
Time complexity in step 4: O(E VE2)= O(VE3)
E is the number of edges, Maximum flow algorithm needs O(VE2)
Notes: Time complexity of Optimal Barrier Coverage Algorithm is dominated by step 4
In step 4, we try to remove …
E times V times E squae

## Slide 37: Conclusions
Barrier Coverage with Optimized Quality Problem is molded and solved in this paper
Aiming at this problem, we proposed a Optimal Barrier Coverage Algorithm (OBCA)
The OBCA is time-efficient (polynomial time complexity)
▆