## Slide 1: Vehicular Networking
An introduction
gugu@ACN-Lab.CSIE.NCU

## Slide 2: Basics
The DSRC

## Slide 3: DSRC Spectrum
Dedicated Short Range Communications – DSRC spectrum
  1999 U.S. FCC granted
  For public safety and non-safety applications
    Non-safety applications are accommodated in the DSRC spectrum to encourage development and deployment of DSRC technology
      Promote cost-efficiency
  75MHz radio frequency band

## Slide 4: DSRC Spectrum

## Slide 5: DSRC Spectrum
Located in the 5.85 – 5.925 GHz
  Divided into seven 10 MHz channels
    Channel 178 – Control Channel (CCH)
      To achieve reliable safety message dissemination
      Supports higher power levels
      Be solely responsible for broadcasting
        Safety related message
        Other service announcements
    Channel 184 – High Available Low Latency (HALL) Channel
      Be left for future use

## Slide 6: DSRC Spectrum
    Channel 172 – unused in most current prototype
    All non-safety communications take place on Service Channels (SCHs)

## Slide 7: DSRC Spectrum
Each communication zone
  Must utilize channel 178 as a CCH
    For safety message
  May utilize one or more SCH of the available four service channels
    Typically used to communicate IP-based services

## Slide 8: WAVE Standard Specification Suite
2004 – IEEE Task Group p started
  Based on IEEE 802.11
  Amendment – IEEE 802.11p
    physical and MAC layers
IEEE started 1609 working group to specify the additional layers
  IEEE 1609.1 – resource manager
  IEEE 1609.2 – security
  IEEE 1609.3 – networking
  IEEE 1609.4 – multi-channel operation

## Slide 9: WAVE Standard Specification Suite
Wireless Access in Vehicular Environments
  IEEE 802.11p + IEEE 1609.x  WAVE

## Slide 10: IEEE 802.11p Phy-1
Specifies the physical and MAC features
  For IEEE 802.11 could work in a vehicular environment
Based on IEEE 802.11a
  Operating in the 5.8/5.9 GHz band
    The same as IEEE 802.11a
  Based on an orthogonal frequency-division multiplexing (OFDM) PHY layer
    The same as IEEE 802.11a

## Slide 11: IEEE 802.11p Phy-2
  Each channel has 10 MHz wide frequency band
    A half to the 20-MHz channel of IEEE 802.11a
  Data rates ranges from 3 to 27 Mb/s
    A half to the corresponding data rates of IEEE 802.11a
      6 to 54 Mb/s
    For 0 – 60 km/hr vehicle speed
      9, 12, 18, 24, and 27 Mbps
    For 60 – 120 km/hr vehicle speed
      3, 4.5, 6, 9, and 12 Mbps
    Lower rates are often preferred in order to obtain robust communication

## Slide 12: IEEE 802.11p Phy-3
The system comprises 52 subcarriers
  Modulation schemes
    BPSK, QPSK, 16-QAM, or 64-QAM
  Coding rate
    1/2, 2/3, or 3/4
  Data rates are determined by the chosen coding rate and modulation scheme

## Slide 13: IEEE 802.11p Phy-4
Single and multiple channel radios
  Single-channel WAVE device
    Exchanges data and/or listens to only one channel at a time
  Multi-channel WAVE device
    Exchanges data on one channel while, at least, actively listening on a second channel
  A synchronization mechanism
    To accommodate the limited capabilities of single channel device
    To allow interoperability between single channel devices and multi-channel

## Slide 14: IEEE 802.11p Phy-5
    To ensure all WAVE devices monitor and/or utilize the CCH at common time intervals
    Both CCH and SCH intervals are uniquely defined with respect to an accurate time reference
    E.g. to CCH/SCH design
Synchronization
  A typical device visit the CCH for a time period – CCH Interval (CCHI)
  Switch to a SCH for a period – SCH Interval (SCHI)
  Guard Interval (GI)
    To accommodate for device differences

## Slide 15: IEEE 802.11p Phy-6
Two popularized synchronization mechanisms
  The earliest received clock signal
  The availability of global clock signal

## Slide 16: IEEE 802.11p Phy-7
The earliest received clock signal mechanism
  Distributed
  Built-in robustness
    Roaming devices can adopt different clock reference as they move to newer communication zone
  Any synchronization failure would be local to devices in a single communication zone
    No concern about nation-wide failure
    No fears of nation-wide attack

## Slide 17: IEEE 802.11p Phy-8
  Little guarantee
    Devices may follow invalid or malicious clock
  Continuously clock drifts result in lesser efficiency in radio resource utilization
Global clock signal mechanism
  Needs sufficient accuracy
  Devices align their radio resources to a globally accurate clock every time period
  Suffers from being too centralized
    Attacks or failure in the global clock leads to wide-spread irrecoverable failure of the DSRC network

## Slide 18: IEEE 802.11p Phy-8
Current WAVE standards follow the global signal approach
  A combination of the global signal and some other distributed approaches is most likely adpoted

## Slide 19: IEEE 802.11p MAC-1
IEEE 802.11p is a member of IEEE 802.11 family
  Inherits CSMA/CA multiple channel access scheme
    Originally the system supports only one-hop broadcasts
  DCF coordination
    Guaranteed quality of service support cannot be given

## Slide 20: IEEE 802.11p MAC-2
Quality of Service guarantee for prioritization
  IEEE 802.11e – enhanced distributed channel access (EDCA) can be used

## Slide 21: IEEE 802.11p MAC-3
Channel Router
  For WAVE Short Message Protocol (WSMP) datagram
    Checking the EtherType field of the 802.2 header
  Then forwards the WSMP datagram to the correct queue based on
    channel identified in the WSMP header
    packet priority
  If the WSMP datagram is carrying an invalid channel number
    discard the packet
      without issuing any error to the sending application

## Slide 22: IEEE 802.11p MAC-4
  For IP datagram
    Before initializing IP data exchanges, the IP application registers the transmitter profile with the MLME
      contains SCH number
      power level
      data rate
      the adaptable status of power level and data rate
    When an IPv6 datagram is passed from the LLC to the Channel Router
      Channel Router routes the datagram to a data buffer that corresponds to the current SCH

## Slide 23: IEEE 802.11p MAC-5
    If the transmitter profile indicates specific SCH that is no longer valid
      the IP packet is dropped
      no error message is issued to originating application
Channel Selector
  carries out multiple decisions as to
    when to monitor a specific channel,
    what are the set of legal channels at a particular point in time
    how long the WAVE device monitors and utilizes a specific channel

## Slide 24: IEEE 802.11p MAC-6
  The Channel Selector also decides to drop data
    if it is supposed to be transmitted over an invalid channel
      E.g. when a channel does not exist any longer

## Slide 25
Thank you for your attendance