## Slide 1: Chapter 6: Conditional Processing
Copyright 1999-2000, Prentice-Hall Incorporated
Updated 10/00
Slides to Accompany
Assembly Language for Intel-Based Computers,
Third Edition

## Slide 2
Overview
Boolean and Comparison Instructions
  AND, OR, XOR, NOT, NEG, TEST
  BT, BTC, BTR, BTS, BSF, BSR
  CMP, CMPXCHG
Conditional Jumps
  Jcond
  SETcond
Conditional Loops
  LOOPZ, LOOPE, LOOPNZ, LOOPNE
High-Level Logic Structures
  IF, compound IF, WHILE, REPEAT, CASE
  Table of procedure offsets
  Finite-State Machines (FSM)

## Slide 3
  Table 1. Boolean Instructions

## Slide 4
Boolean AND Operation
The following is a truth table, showing the results of ANDing individual bits:
 | 1 | 0
1 | 1 | 0
0 | 0 | 0
bit-1
bit-2

## Slide 5
AND Instruction
op-1: 1 1 0 1 0 0 1 1
op-2: 0 1 0 0 1 1 0 1
result: 0 1 0 0 0 0 0 1
Each bit in the result is created by ANDing each of the input bits in the same positions:

## Slide 6
AND Instruction
Performs a boolean AND operation between each of the corresponding bits in two operands and places the result in the first operand:
and ax,bx
and var1,edx
and bl,var2
and dx,02FAh
and al,00001111b
target
source

## Slide 7
AND Instruction
Example: the following will jump to the label PrinterReady if bits 0, 1, and 2 are all set in the AL register:
and al,00000111b
cmp al,00000111b
je PrinterReady
.
.
PrinterReady:

## Slide 8
Boolean OR Operation
The following is a truth table, showing the results of ORing individual bits:
 | 1 | 0
1 | 1 | 1
0 | 1 | 0
bit-1
bit-2

## Slide 9
OR Instruction
op-1: 1 1 0 1 0 0 1 1
op-2: 0 1 0 0 1 1 0 1
result: 1 1 0 1 1 1 1 1
Each bit in the result is created by ORing each of the input bits in the same positions:

## Slide 10
OR Instruction
Performs a boolean OR operation between each of the corresponding bits in two operands and places the result in the first operand:
or ax,bx
or var1,edx
or bl,var2
or dx,02FAh
or al,00001111b
target
source

## Slide 11
OR Instruction
Example: the CapsLock key corresponds to bit 6 in the keyboard status byte. The following turns on the CapsLock key.
mov ax,40h ; DOS data segment
mov ds,ax
mov bx,0017h ; keyboard status byte
or byte ptr[bx],01000000b

## Slide 12
Boolean XOR Operation
The following is a truth table, showing the results of XORing individual bits:
 | 1 | 0
1 | 0 | 1
0 | 1 | 0
bit-1
bit-2

## Slide 13
XOR Instruction
op-1: 1 1 0 1 0 0 1 1
op-2: 0 1 0 0 1 1 0 1
result: 1 0 0 1 1 1 1 0
Each bit in the result is created by XORing each of the input bits in the same positions:
(XOR yields a 1 only when the two input bits are different.)

## Slide 14
XOR Instruction
mov al,10110011b
xor al,11111111b ; AL = 01001100
XORing any bit with 1 toggles (inverts) the bit:
XORing any bit with 0 leaves the bit unchanged:
mov al,10110011b
xor al,00000000b ; AL = 10110011

## Slide 15
XOR Instruction
mov al,10110011b
xor al,10101100b ; AL = 00011111
xor al,10101100b ; AL = 10110011
The XOR operation reverses itself. It is particularly well suited to inverting graphic images.
same

## Slide 16
NOT Instruction
Performs a boolean NOT (inversion) operation on each of the bits in the operand.
mov bh,11001101b
not bh ; bh = 00110010

## Slide 17
NEG Instruction
Converts the operand to its twos complement. It's a good idea to check the Overflow flag after performing a NEG operation.
mov bl,00000001b
neg bl ; bl = 11111111
mov ah,11001101b
neg ah ; ah = 00110011
mov al,-128
neg al ; al = 80h, OF=1

## Slide 18
TEST Instruction
Performs an implied AND operation between corresponding bits in the two operands. Only the flags are affected.
mov bl,00000001b
test bl,00000001b ; ZF = 0
mov ah,11001101b
test ah,00110010b ; ZF = 1

## Slide 19
TEST Instruction
Example: the following will jump to the label PrinterReady if either bit 0, 1, or 2 is set in the AL register:
test al,00000111b
jnz PrinterReady
.
.
PrinterReady:

## Slide 20
  Table 2. BT, BTC, BTR, and BTS Instructions

## Slide 21
CMP Instruction
mov ax,5
cmp ax,5 ; ax == 5
cmp ax,7 ; ax < 7
cmp ax,3 ; ax > 3
Performs an implied subtraction of the source operand from the target operand. Only the flags are affected.
target
source

## Slide 22
Flags Set by the CMP Instruction
Signed:
Unsigned:

## Slide 23
Example 1. Using the CMP Instruction
  Label1:
  mov al,5
  cmp al,10 ; CF=1, ZF=0
  Label2:
  mov ax,1000
  mov cx,1000
  cmp cx,ax ; CF=0, ZF=1
  Label3:
  mov si,105
  cmp si,0 ; CF=0, ZF=0

## Slide 24
Table 3. Do-While Loop Example

## Slide 25
Table 4. Jumps Based on General Comparisons

## Slide 26
Table 5. Jumps Based on Unsigned Comparisons

## Slide 27
Table 6. Jumps Based On Signed Comparisons

## Slide 28
  1: mov small,al ; assume AL is the smallest
  2: cmp small,bl ; if small <= BL then
  3: jbe L1 ; jump to L1
  4: mov small,bl ; else move BL to small
  5: L1: cmp small,cl ; if small <= CL then
  6: jbe L2 ; jump to L2
  7: mov small,cl ; else move CL to small
  8: L2:
Finding the Smallest of Three Integers

## Slide 29
Ex 3. Single Character Encryption Using XOR
  XORVAL = 239 ; any value between 0–255
  .code
  main proc
  mov ax,@data
  mov ds,ax
  L1: mov ah,6 ; direct console input
  mov dl,0FFh ; don’t wait for character
  int 21h ; AL = character
  jz L2 ; quit if ZF = 1 (EOF)
  xor al,XORVAL
  mov ah,2 ; write to output
  mov dl,al
  int 21h
  jmp L1 ; repeat the loop
  L2: mov ax,4C00h ; return to DOS
  int 21h
  main endp
  end main

## Slide 30
Example 4. Testing the Isalpha Procedure (1 of 2)
  title Test Alphabetic Input (ISALPHA.ASM)
  ; This program reads and displays characters
  ; until a non–alphabetic character is entered.
  .model small
  .stack 100h
  .code
  main proc
  mov ax,@data
  mov ds,ax
  L1: mov ah,1 ; input a character
  int 21h ; AL = character
  call Isalpha ; test value in AL
  jnz exit ; exit if not alphabetic
  jmp L1 ; continue loop
  exit:
  mov ax,4C00h ; return to DOS
  int 21h
  main endp

## Slide 31
Example 4. Testing the Isalpha Procedure (2 of 2)
  ; Isalpha sets ZF = 1 if the character
  ; in AL is alphabetic.
  Isalpha proc
  push ax ; save AX
  and al,11011111b ; convert to uppercase
  cmp al,’A’ ; check ‘A’...’Z’ range
  jb B1
  cmp al,’Z’
  ja B1
  test ax,0 ; ZF = 1
  B1: pop ax ; restore AX
  ret
  Isalpha endp
  end main

## Slide 32
Largest and Smallest Signed Array Values
  count = 0
  smallest = array[count]
  largest = array[count]
  CX = 6
  do while CX > 0
  AX = array[count]
  if (AX < smallest) then smallest = AX
  if (AX > largest) then largest = AX
  count = count + 1
  CX = CX - 1
  end do
Pseudocode for a simple loop that finds the largest and smallest values in an array:

## Slide 33
Ex 5. Largest and Smallest Signed Array Values (1 of 4)
  .data
  largest dw ?
  smallest dw ?
  array dw –1,2000,–421,32767,500,0,–26,–4000
  arrayCount = ($-array) / (type array)
  largemsg db "Largest value: ",0
  smallmsg db "Smallest value: ",0
Here is the algorithm implemented in an assembly language program:

## Slide 34
Ex 5. Largest and Smallest Signed Array Values (2 of 4)
  .code
  extrn Clrscr:proc, Crlf:proc, Writeint_signed:proc, \
  Writestring:proc
  main proc
  mov ax,@data ; initialize DS
  mov ds,ax
  mov di,offset array
  mov ax,[di] ; get first element
  mov largest,ax ; initialize largest
  mov smallest,ax ; initialize smallest
  mov cx,arrayCount ; loop counter
  A1: mov ax,[di] ; get array value
  cmp ax,smallest ; [DI] >= smallest?
  jge A2 ; yes: skip
  mov smallest,ax ; no: move [DI] to smallest

## Slide 35
Ex 5. Largest and Smallest Signed Array Values (3 of 4)
  A2: cmp ax,largest ; [DI] <= largest?
  jle A3 ; yes: skip
  mov largest,ax ; no: move [DI] to largest
  A3: add di,2 ; point to next number
  loop A1 ; repeat the loop until CX=0
  call ShowResults
  mov ax,4C00h ; return to DOS
  int 21h
  main endp

## Slide 36
Example 5. Largest and Smallest Signed Array Values (4 of 4)
  ; Display the largest and smallest values.
  ShowResults proc
  mov dx,offset largemsg ; largest
  call Writestring
  mov ax,largest
  call Writeint_signed
  call CrLf
  mov dx,offset smallmsg ; smallest
  call Writestring
  mov ax,smallest
  call Writeint_signed
  call CrLf
  ret
  ShowResults endp
  end main

## Slide 37
SETcondition Instruction
setz al ; set AL to 1 if ZF = 1
sete al ; set AL to 1 if ZF = 1
setnc myFlag ; set myFlag to 1 if CF = 0
setae myFlag ; set myFlag to 1 if CF = 0
setge byte ptr [si] ; set [si] to 1 if SF = OF
setnbe byte ptr [si] ; set [si] to 1 if SF = OF
The SETcondition instruction sets a byte operand to 1 if a given condition is true, or to 0 if the condition is false. Here are examples:

## Slide 38
Conditional Loops (LOOPZ and LOOPE)
.data
intarray dw 0,0,0,0,1,20,35,–12,66,4,0
ArraySize = ($–intarray) / (type intarray)
.code
mov bx,offset intarray ; point to the array
sub bx,2 ; back up one position
mov cx,ArraySize ; repeat ArraySize times
next:
add bx,2 ; point to next entry
cmp word ptr [bx],0 ; compare value to zero
loopz next ; while ZF=1 and CX > 0
The LOOPZ and LOOPE instructions allow a loop to continue if ZF =1 and CX > 0. The following example scans an array looking for a nonzero value:

## Slide 39
Conditional Loop Example
next:
cmp [bx],ax ; compare array value to zero
add bx,2 ; point to next entry, ZF = 0
loopz next ; error: Zero flag has changed
Be careful not to modify the flags prior to to a conditional LOOP instruction:

## Slide 40
LOOPNZ and LOOPNE
.data
bytearray db ‑3,‑6,‑1,‑10,10,30,40,4
ArraySize = ($–array)
.code
mov si,offset bytearray‑1
mov cx,ArraySize
next:
inc si
test byte ptr [si],10000000b
loopnz next
The LOOPNZ and LOOPNE instructions continue the loop as long as ZF=0 and CX > 0. The following loop scans an array until a positive integer is found:

## Slide 41
High-Level Logic Structures
IF Statement
Compound IF Using OR
Compound IF Using AND
Loops
  WHILE Loop
  DO-WHILE Loop
  REPEAT-UNTIL Loop
CASE Structure

## Slide 42
Simple IF Statement
cmp ax,op2
je True
jmp EndIf
True:
mov flag,1
mov count,0
EndIf:
Pseudocode:
if (AX = op2) then
mov flag,1
mov count,0
end if
Implementation:

## Slide 43
Simple IF Statement (alternate form)
cmp ax,op2
jne EndIf
mov flag,1
mov count,0
EndIf:
Pseudocode:
if (AX = op2)
mov flag,1
mov count,0
end if
Implementation:
Reversing the condition enables you to shorten the implementation by one instruction.

## Slide 44
Compound IF Statement Using OR
cmp al,op1
jg L1
cmp al,op2
jge L1
cmp al,op3
je L1
jmp L2
L1: mov flag,1
mov count,5
L2:
Pseudocode:
if (AL > op1)
or (AL >= op2)
or (AL = op3)
mov flag,1
mov count,5
end if
Implementation:

## Slide 45
Compound IF Statement Using AND
Pseudocode:
if (AL > op1)
and (AL >= op2)
and (AL = op3)
mov flag,1
mov count,5
end if
Implementation:
cmp al,op1
jng L1
cmp al,op2
jnge L1
cmp al,op3
jne L1
mov flag,1
mov count,5
L1:

## Slide 46
Combining AND and OR
Pseudocode:
if (AL > op1)
and (AL >= op2)
or (AL = BL)
mov flag,1
mov count,5
end if
Implementation:
cmp al,op1
jng L1
cmp al,op2
jnge L1
jmp L2
L1: cmp al,bl
jne L3
L2: mov flag,1
mov count,5
L3:

## Slide 47
Ex 6. Do-While Loop Example
  Assembly Code Pseudocode
  while:
  cmp op1,op2 do while (op1 < op2)
  jnl L3
  <statement1> <statement1>
  cmp op2,op3 if op2 = op3 then
  jne L1
  <statement2> <statement2>
  <statement3> <statement3>
  jmp L2 else
  L1: <statement4> <statement4>
  L2: jmp while endif
  L3: enddo

## Slide 48
6.4.4. Repeat-Until Structure
  repeat:
  <statement1>
  <statement2>
  <statement3>
  until (op1 = op2) or (op1 > op3)
Code this loop in assembly language:
Given the following structure...

## Slide 49
Repeat-Until Loop
  1: repeat:
  2: <statement1>
  3: <statement2>
  4: <statement3>
  5: test1:
  6: cmp op1,op2 ; if op1 = op2 then
  7: je endif ; exit the loop
  8: test2: ; else
  9: cmp op1,op3 ; if op1 <= op3 then
  10: jng repeat ; repeat the loop
  11: endif: ; end if
  12: ; end if

## Slide 50
6.4.5 CASE Structure
  case input of
  'A' :Process_A;
  'B' :Process_B;
  'C' :Process_C;
  'D' :Process_D;
  end;
The CASE structure allows a multiway branch by comparing a single value to a list of values. This example is taken from Pascal:

## Slide 51
Implementing the Case in Assembly Language
mov al,input ; case al of
cmp al,’A’ ; ‘A’:
je Process_A ; goto Process_A
cmp al,’B’ ; ‘B’:
je Process_B ; goto Process_B
cmp al,’C’ ; ‘C’:
je Process_C ; goto Process_C
cmp al,’D’ ; ‘D’:
The most direct implementation involves CMP and conditional jump instructions:
But you can also call procedures and jump to an ending label:

## Slide 52
Ex 9. Case Structure Using Procedure Calls
  mov al,input ; case al of
  cmp al,’A’ ; ‘A’:
  jne L1
  call Process_A ; call Process_A
  jmp L4 ; jump to L4
  L1: cmp al,’B’ ; ‘B’:
  jne L2
  call Process_B ; call Process_B
  jmp L4 ; jump to L4
  L2: cmp al,’C’ ; ‘C’:
  jne L3
  call Process_C ; call Process_C
  jmp L4 ; jump to L4
  L3: cmp al,’D’ ; ‘D’:
  jne L4
  call Process_D ; call Process_D
  L4: ; end

## Slide 53
Ex 10. Table Containing Offsets of Procedures
CaseTable db ‘A’ ; lookup value
dw process_A ; address of procedure
db ‘B’
dw process_B
db ‘C’
dw Process_C
db ‘D’
dw Process_D
A table may contain lookup values and corresponding procedure offsets. Unlike a case structure, this table can be modified at runtime.

## Slide 54
Fig 1. Table of Procedure Offsets
Let's assume that four different procedures are located at offsets 0120, 0130, 0140, and 0150, respectively. This is how the table would look in memory:

## Slide 55
Ex 11. Case Table Lookup Using a Loop
  NumberOfEntries = 4
  input dw ?
  .code
  mov al,input ; value to be found
  mov bx,offset CaseTable ; point BX to the table
  mov cx,NumberOfEntries ; loop counter
  L1: cmp al,[bx] ; match found?
  jne L2 ; no: continue
  call word ptr [bx+1] ; yes: call the procedure
  jmp L3 ; exit the search
  L2: add bx,3 ; point to next entry
  loop L1 ; repeat until CX = 0
  L3:
When AL matches a character in the table, the following code calls the procedure whose address is located in the table immediately following the matching character:

## Slide 56
Fig 2. Finite-State Machine
A finite-state machine (FSM) is a connected graph consisting of nodes and directed arcs. Each arc shows a possible transition between states, and each node represents a state.
(terminal state)

## Slide 57
Fig 3. FSM for a String Beginning With X and Ending with Z
Sample matching strings:
xaabcfgz xuytrz xz xaaaaaaz xerwoiuoeruoxz xyyyaaayayaz

## Slide 58
Figure 4. Signed Decimal Integer FSM
Sample matching strings:
+2 -4 234 6 +876 -549

## Slide 59
Ex 12. FSM for Signed Decimal Input (1 of 5)
  Title Finite State Machine (fsm.asm)
  ; Chapter 6 example. Implementation of finite
  ; state machine that accepts an integer with an
  ; optional leading sign.
  .model small
  .stack 100h
  DOS_CHAR_INPUT = 1
  ENTER_KEY = 0Dh
  .data
  InvalidInputMessage db "Invalid input",0dh,0ah,0

## Slide 60
Ex 12. FSM for Signed Decimal Input (2 of 5)
  .code
  extrn Writestring:proc, Crlf:proc, Clrscr:proc
  main proc
  mov ax,@data
  mov ds,ax
  call Clrscr
  StateA:
  call Getnext ; read next char into AL
  cmp al,’+’ ; leading + sign?
  je StateB ; go to State B
  cmp al,’–’ ; leading – sign?
  je StateB ; go to State C
  call Isdigit ; ZF = 1 if AL contains a digit
  jz StateC
  call DisplayError ; invalid input found
  jmp Exit

## Slide 61
Ex 12. FSM for Signed Decimal Input (3 of 5)
  StateB:
  call Getnext ; read next char into AL
  call Isdigit ; ZF = 1 if AL contains a digit
  jz StateC
  call DisplayError ; invalid input found
  jmp Exit
  StateC:
  call Getnext ; read next char into AL
  jz Exit ; quit if Enter pressed
  call Isdigit ; ZF = 1 if AL contains a digit
  jz StateC
  call DisplayError ; invalid input found
  jmp Exit
  Exit:
  call Crlf
  mov ax,4c00h
  int 21h
  main endp

## Slide 62
; Read char from standard input into AL,
; set ZF = 1 if Enter key was read.
  Getnext proc
  mov ah,DOS_CHAR_INPUT ; read standard input
  int 21h ; AL = character
  cmp al,ENTER_KEY
  ret
  Getnext endp
  ; Set ZF = 1 if the character in AL is a digit.
  Isdigit proc
  cmp al,’0'
  jb A1
  cmp al,’9'
  ja A1
  test ax,0 ; set ZF = 1
  A1: ret
  Isdigit endp
Ex 12. FSM for Signed Decimal Input (4 of 5)

## Slide 63
Ex 12. FSM for Signed Decimal Input (5 of 5)
  ; Display error message.
  DisplayError proc
  push dx
  mov dx,offset InvalidInputMessage
  call WriteString
  call Crlf
  pop dx
  ret
  DisplayError endp
  end main

## Slide 64
Table 7. Conditional Jumps, Flag Settings (Question 9)

## Slide 65
The End