## Slide 1: Energy Harvesting Technologies and Charger Deployment for Wireless Rechargable Sensor Networks
by Professor Jehn-Ruey Jiang from NCU, Taiwan

## Slide 2: Part 1: Energy Harvesting Technologies

## Slide 3: Energy Harvesting
Source: http://technologygreenenergy.blogspot.tw/2013/11/type-of-energy-sources.html
Notes: http://technologygreenenergy.blogspot.tw/2013/11/type-of-energy-sources.html

## Slide 4: Types of Energy Harvesting
Energy harvesting
Radiant energy
Mechanical energy
Thermal energy
Magnetic Induction
Solar power
RF
Body heat Water heat
Other heat
Treading
Vibrations
Air flow

## Slide 5
Thermal energy

## Slide 6: Thermoelectric Effect
Through thermoelectric effect, heat can be transformed into electricity.
Notes: 出處: http://experiment.phys.nchu.edu.tw/device/exp44.html

## Slide 7: Body Heat

## Slide 8: Body Heat

## Slide 9: Water Heat
New thermoelectric material sucks electricity out of hot water

## Slide 10: Other heat
Cup of coffee too hot? Harvest some of that waste energy to charge your gadgets.

## Slide 11
Mechanical energy

## Slide 12: Piezoelectric Effect
Through piezoelectric effect, electricity is generated when a piezoelectric plate vibrates (or is pressed/released).
Notes: 出處網址: (1) http://zh.wikipedia.org/wiki/%E5%A3%93%E9%9B%BB%E6%95%88%E6%87%89
(2) http://www.aurumtec.com.tw/DB/Technology/%E5%A3%93%E9%9B%BB%E6%95%88%E6%87%89.htm
(3) http://highscope.ch.ntu.edu.tw/wordpress/?p=3331

## Slide 13: Treading

## Slide 14: Treading

## Slide 15: Vibrations
When we flap the plate, the plate vibrates and we gain electricity.
Notes: When you flap the plate, the plate vibrate and you gain electricity.
出處網址: (1) http://www.cpr.cuhk.edu.hk/tc/press_detail.php?id=190
(2) http://www.nippon.com/hk/views/b01502/
振動能為再生能源的一種，遍布日常生活環境中，例如汽車及火車行駛時的顛簸、車流經過公路及橋樑時所引起的輕微振動，都可產生振動 能量，而壓電材料則可收集這些環境中的振動能量。
當壓電材料因振動而受拉或受壓時，部分振動機械能量就會轉化成電能，並可儲存在收集器內。

## Slide 16: Air Flow
A flapping leaf generator for air-flow energy harvesting

## Slide 17
Radiant energy

## Slide 18: Magnetic Induction

## Slide 19: Magnetic Induction
Magnetic Induction (MI)
Change in the magnetic flux of the left coil induces a current in the right coil.
Notes: 出處網址: http://www.technical-direct.com/2013-05/%E7%84%A1%E7%B7%9A%E5%85%85%E9%9B%BB%E6%8A%80%E8%A1%93%EF%BC%88wireless-charging%EF%BC%89%E6%93%BA%E8%84%AB%E9%BA%BB%E7%85%A9%E5%85%85%E9%9B%BB%E5%99%A8%E5%AF%A6%E7%8F%BE%E7%84%A1%E9%99%90%E5%8F%AF/

## Slide 20: Solar Power

## Slide 21: Photovoltaic Effect
Photovoltaic Effect
Through photovoltaic effect, light energy is transformed into electricity.
Notes: 出處網址: http://zh.wikipedia.org/wiki/%E5%85%89%E7%94%9F%E4%BC%8F%E6%89%93%E6%95%88%E5%BA%94

## Slide 22: Xenon
The spectrum of a xenon lamp approximates that of the sun. So, it can be used as an “indoor solar power source.”

## Slide 23: RF Power Sources
Notes: RF Power Sources

## Slide 24: Ambient (Anticipated or Unknown) RF
Ambient RF
The credit-card-sized device can suck power out of the air from TV, cellular transmissions, and other RF signals.
Notes: 出處: http://www.extremetech.com/extreme/160634-ambient-backscatter-free-energy-harvesting-from-tv-signals-to-power-a-ubiquitous-internet-of-things

## Slide 25
Intentional RF - WISP (wireless identification and sensing platform)
Reader
Tag
Notes: WISP tag具備優點:
能偵測環境
通訊方面相容於UHF RFID Tag
可程式化
被動式，無須電池供電

## Slide 26
WISP Tag
Properties
UHF RFID Tag
Passive
Programmable
Onboard sensors
Notes: WISP tag具備優點:
能偵測環境
通訊方面相容於UHF RFID Tag
可程式化
被動式，無須電池供電

## Slide 27: WISP Tag
Passive Data Logger (PDL) Tag
Power Management
Antenna
Analog Front End
Storage Capacitor
Microcontroller
Sensor
Flash Memory
RFID Reader
Notes: WISP tag的構造:
天線
類比前端
電容，儲存電力
微控制器
快閃記憶體
感測器
實際上天線佔大部分面積 (最下面的方塊圖)

## Slide 28
Reader
Tag
Tag Memory
EPC ID
ID Memory
User Memory
Sensor Data
Charge remaining
Time elapsed since last reset
Historical Sensor Measurements
Fully compatible with EPC Gen 2 specification
Compatible with EPC G2 tags
Notes: Electronic Product Code™ - EPC
Gen 2 可讀寫多次 (且具大容量記憶體)，故將Tag Memory分成ID Memory與User Memory兩部分。
ID memory相當於該tag的身分證。
User Memory 存放感測資料。

## Slide 29: Intentional RF – Charger and Harvester

## Slide 30: Powercast Technology Overview
Trickle-charging means to charge a fully charged battery under no-load at a rate equal to its self-discharge rate, thus enabling the battery to remain at its fully charged level.
Notes: Powercast Technology Overview

## Slide 31: Powercast Recommended Power Profiles
Notes: Recommended Power Profiles

## Slide 32: Powercast Charger TX91501
915 MHz center frequency
FCC and IC certified
1W or 3W EIRP (Equivalent Isotropically Radiated Power)
– TX91501-1W-ID
– TX91501-3W-ID
~60° beam pattern
Plug-and-play installation
Power virtually unlimited number of harvesters
Notes: Federal Communications Commission (FCC)
IC (Industry Canada)
1.甚麼是trickle-charging batteries
A: 『涓流充電電池』，意思是當電池充飽了以後，仍以微弱的電力繼續對電池充電，以防電池電力隨時間自然衰減。
4. configurable and regulated
A: power harvester是能夠調整輸出的電壓與電流的。
5. RoHS compliant
A: RoHS認證，RoHS Directive方面，歐盟議會和歐盟部長級理事會一致同意自2006年7月起禁止在電子電器設備中使用鉛、鎘、汞、鉻（hexavalent chromium）等四種重金屬以及PBB和PBDE等兩種溴化物阻燃劑（brominated flame retardant）。且於2011年7月1日歐盟官方期刊上正式公布RoHS指令修訂版(2011/65/EU)，並於2011年7月21日生效、2013年1月3日正式取代/廢止舊指令(2002/95/EC)。
6. DSSS
A: Direct-sequence spread spectrum（直接序列展頻技術），將原本”0”與”1”的高功率、窄頻寬的位元訊號，透過虛擬隨機序列(Pseudo Random Sequence)和相位移轉技術（PSK；Phase Shift Keying），轉變成低功率、寬頻帶（在2.4Ghz頻帶，分以13個頻道，每個頻道頻寬為5MHz）的載波訊號，這些轉變後的載波訊號被稱為Spreading Chips，Chips數愈多可以增加資料安全性，愈低則增加使用者數目。一般普遍使用10-20 Chips。
7. EIRP
A: 等效全向輻射功率 (Equivalent Isotropically Radiated Power; EIRP)，射頻的天線發送出的功率（P）和該天線增益（G）的乘積，即： EIRP=P*G，
如果用dB計算，則為EIRP(dBW) = P(dBW) + G(dBW) ，EIRP 表示了發送功率和天線增益的聯合效果。
8. TX91501-1W-ID
A: Powercast的無線充電器的輸出功率分為兩種，TX91501-1W-ID即輸出功率為1W; 實驗室買的是TX91501-3W-ID即輸出功率為3W。

## Slide 33: Power Harvester P2110CSR-EVB
Convert RF input to DC current
Frequency range: 850-950MHz
Output voltage: 1.8V to 5.25V
(configurable)
Range of at least 3 meters

## Slide 34: Experiment
Distance R
Normal vector

## Slide 35: Experiment
R / |  |  |  |  |  |  | 
0.5 m | 4.21 | 4.21 | 4.21 | 4.20 | 4.20 | 4.20 | 4.20
1.0 m | 4.21 | 4.21 | 4.21 | 4.20 | 4.20 | 4.20 | 0.02
1.5 m | 4.21 | 4.21 | 4.21 | 4.21 | 3.04 | 2.01 | 0.02
2.0 m | 4.21 | 4.21 | 4.20 | 4.19 | 1.30 | 1.01 | --
2.5 m | 4.20 | 4.19 | 2.90 | 2.46 | 0.82 | 0.02 | --
3.0 m | 2.74 | 2.39 | 1.88 | 0.73 | 0.01 | -- | --
3.5 m | 1.01 | 0.03 | 0.02 | 0.03 | -- | -- | --
4.0 m | 0.04 | -- | -- | -- | -- | -- | --
0.5 m | 4.21 | 4.21 | 4.21 | 4.20 | 4.20 | 4.20 | 4.20
1.0 m | 4.21 | 4.21 | 4.21 | 4.20 | 4.20 | 4.20 | 0.02
1.5 m | 4.21 | 4.21 | 4.21 | 4.21 | 3.04 | 2.01 | 0.02
2.0 m | 4.21 | 4.21 | 4.20 | 4.19 | 1.30 | 1.01 | --
2.5 m | 4.20 | 4.19 | 2.90 | 2.46 | 0.82 | 0.02 | --
3.0 m | 2.74 | 2.39 | 1.88 | 0.73 | 0.01 | -- | --
3.5 m | 1.01 | 0.03 | 0.02 | 0.03 | -- | -- | --
4.0 m | 0.04 | -- | -- | -- | -- | -- | --
Voltage (V) and distance (m) between

## Slide 36: Experiment (Cont.)
Chart: 
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4
deg 0 | 4.21 | 4.21 | 4.21 | 4.21 | 4.2 | 2.74 | 1.01 | 0.04
deg 15 | 4.21 | 4.21 | 4.21 | 4.21 | 4.19 | 2.39 | 0.03
deg 30 | 4.21 | 4.21 | 4.21 | 4.2 | 2.9 | 1.88 | 0.02
deg 45 | 4.2 | 4.2 | 4.21 | 4.19 | 2.46 | 0.73 | 0.03
deg 60 | 4.2 | 4.2 | 3.04 | 1.3 | 0.82 | 0.01
deg 75 | 4.2 | 4.2 | 2.01 | 1.01 | 0.02
deg 90 | 4.2 | 0.02
Distance (m)
Voltage (V)

## Slide 37: Experiment (Cont.)
R / |  |  |  |  |  |  | 
0.5 m | 35.5 | 33.6 | 26.9 | 22.7 | 12.8 | 4.20 | 2.52
1.0 m | 7.80 | 7.65 | 4.84 | 2.94 | 1.85 | 0.49 | 0.03
1.5 m | 4.50 | 3.58 | 2.99 | 1.98 | 0.18 | -- | --
2.0 m | 2.78 | 2.36 | 2.04 | 1.44 | -- | -- | --
2.5 m | 1.31 | 0.96 | 0.79 | 0.38 | -- | -- | --
3.0 m | 0.75 | 0.44 | 0.37 | -- | -- | -- | --
3.5 m | 0.07 | -- | -- | -- | -- | -- | --
0.5 m | 35.5 | 33.6 | 26.9 | 22.7 | 12.8 | 4.20 | 2.52
1.0 m | 7.80 | 7.65 | 4.84 | 2.94 | 1.85 | 0.49 | 0.03
1.5 m | 4.50 | 3.58 | 2.99 | 1.98 | 0.18 | -- | --
2.0 m | 2.78 | 2.36 | 2.04 | 1.44 | -- | -- | --
2.5 m | 1.31 | 0.96 | 0.79 | 0.38 | -- | -- | --
3.0 m | 0.75 | 0.44 | 0.37 | -- | -- | -- | --
3.5 m | 0.07 | -- | -- | -- | -- | -- | --
Current (mA) and distance (m) between

## Slide 38: Experiment (Cont.)
Distance (m)
Current (mA)
Chart: 
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5
deg 0 | 35.5 | 7.8 | 4.5 | 2.78 | 1.31 | 0.75 | 0.07
deg 15 | 33.6 | 7.65 | 3.58 | 2.36 | 0.96 | 0.44
deg 30 | 26.9 | 4.84 | 2.99 | 2.04 | 0.79 | 0.37
deg 45 | 22.7 | 2.94 | 1.98 | 1.44 | 0.38
deg 60 | 12.8 | 1.85 | 0.18
deg 75 | 4.2 | 0.49
deg 90 | 2.52 | 0.03

## Slide 39: Powercast Charger Effective Charging Area
Powercast wireless charger
Powercast energy harvester
3 m

## Slide 40: Wireless Rechargable Sensor Network
Charger
+ Harvester
+ WSN (wireless sensor network)
= WRSN (wireless rechargable sensor network)

## Slide 41: Part 2: Charger Deployment for Wireless Rechargable Sensor Networks

## Slide 42: Part 2: Outline
Introduction
Problem Definition
Methods
Simulation
Conclusion

## Slide 43: WSN: Wireless Sensor Network
Sensing Range
Communication Range
Sensor Node
Sink Node

## Slide 44: Wireless Sensor Node Examples
A wireless sensor node is a device integrating sensing, communication, and computation. It is usually powered by batteries.

## Slide 45: Wireless Sensor Node Example: Octopus II
Developed in National Central University and National Tsin Hua University
MCU: TI MSP430, 16-bit RISC microcontroller core @ 8Mz
Memory: 40KB in-system programmable flash,10KB RAM, 1MB expandable flash
RF: Chipcon CC2420, 2.4 GHz 802.15.4 (Zigbee) Transceiver (250KBps) (~450m)
Sensing Module: Temperature sensor, Light sensors, Gyroscope, 3-Axis accelerometer
Power: 2 AA battery
+
=
MCU+Memory+RF
Sensing Module

## Slide 46: WSN Application Example
Temperature
Humidity
…
Temperature
Humidity
…
Temperature
Humidity
…
Temperature
Humidity
…
Temperature
Humidity
…

## Slide 47: Q: How to make WSNs sustainable?
(hour)

## Slide 48: A: WSN + RF Charger Energy Harvesting
Energy Harvester
Energy-DC
Energy Source: Charger

## Slide 49: Wireless Charging Model
Charger
Sensor Node
Charging
Distance
Symmetrical Axis Vector
=

## Slide 50: Scenario and Goals
Assumption:
L
W
H
G
Goal: Cover all sensor nodes with the minimum number of chargers to reduce the charger deployment cost.
Sensor nodes in the WRSN can be located on the ground or object surfaces in a cuboid.
The wireless chargers are assumed to be deployed at grid points on a grid of side length G.
Each grid point allows the deployment of several wireless chargers, each equipped with a directional antenna with an adjustable orientation.
Every node can decide the maximum number of chargers needed to make it sustainable.

## Slide 51: Our Goal
Cover all sensor nodes with the minimum number of chargers to make the WRSN sustainable while keeping an as low as possible charger deployment cost.

## Slide 52: Our proposed methods
NB-GCS (Node Based Greedy Cone Selection)
PB-GCS (Pair Based Greedy Cone Selection)
Two greedy heuristic algorithms to minimize the number of chargers.

## Slide 53: Candidate cone generation for NB-GCS
g
A
B
C
D
E
Charging
Distance
Grid Point
For each grid point, first select the sensor nodes within its sphere coverage.
Then generate a vector for each node as the charger cone’s symmetric axis (or orientation).
Notes: 0917-342-520

## Slide 54: Candidate cone generation for NB-GCS
g
A
B
C
D
E
Each vector stands for a cone.
For each cone, try to adjust its orientation for the cone to cover more nodes.

## Slide 55: Candidate cone generation for NB-GCS
A
B
C
D
E
g
The cone orientation adjustment is done by unit vector summation.

## Slide 56: Candidate cone generation for NB-GCS
A
B
C
D
E
g
Parallel with

## Slide 57: Candidate cone generation for NB-GCS
g
A
B
C
D
E
Iterations for node A stops if the cone orientation adjustment cannot make the cone cover more nodes.

## Slide 58: Candidate cone generation for PB-GCS
g
A
B
C
D
E
Charging
Distance
Grid Point
For each grid point, first select the sensor nodes within its sphere coverage.
Then generate a vector for each node as the charger cone’s symmetric axis (or orientation).
Then for each pair of nodes (or vectors), generate candidate cones.

## Slide 59: Candidate cone generation for PB-GCS
g
i
j
g
j
i
1
Unit sphere
r
r
1
Unit sphere
r
Mapping each vector onto g’s unit sphere.
There are three cases to consider.

## Slide 60: Candidate cone generation for PB-GCS
g
j
i
i
j
1
Unit sphere
r

## Slide 61: Greedy cone selection for both methods
C
A
B
D
C1
C2
C3
C1 | C2 | C3
4 | 3 | 1
A | B | C | D
1 | 1 | 1 | 2
#sensor a cone can cover
#chargers needed by a sensor
Return set is empty initially

## Slide 62: Greedy cone selection for both methods
C
A
B
D
C2
C3
C1 | C2 | C3
0 | 0 | 1
A | B | C | D
0 | 0 | 0 | 1
C1

## Slide 63: Greedy cone selection for both methods
C
A
B
D
C2
C1 | C2 | C3
0 | 0 | 0
A | B | C | D
0 | 0 | 0 | 0
C3
C1
Finish!

## Slide 64: Simulation
Item | Parameter
Region | 20 x 15
#Sensors | 50, 100, 150, 200, 250
Effective Charging Distance | 3.0
Angle Threshold | 
The Height of the Deployment Plane | 2.3
Grid Length | 1.0, 1.4, 1.8
Simulator | C++
Item | Parameter
Region | 
#Sensors | 50, 100, 150, 200, 250
Effective Charging Distance | 
Angle Threshold | 
The Height of the Deployment Plane | 
Grid Length | 
Simulator | C++

## Slide 65: Simulation
#chargers
#sensors
Chart: 
| 50 | 100 | 150 | 200 | 250
PB-GCS: 100%-0% | 26 | 36 | 44 | 50 | 53
NB-GCS: 100%-0% | 32 | 46 | 53 | 60 | 62
The most ideal case of 100%-0%, in which all sensor nodes need the 1-coverage requirement
grid length = 1

## Slide 66: Simulation
#chargers
#sensors
Chart: 
| 50 | 100 | 150 | 200 | 250
NB-GCS: 80%-20% | 32 | 47 | 60 | 69 | 78
PB-GCS: 80%-20% | 31 | 41 | 49 | 60 | 69
80% of nodes require 1-coverage and 20% of
nodes require 2-covearge of chargers.
grid length = 1

## Slide 67: Simulation
grid length
#chargers
Chart: 
| 1 | 1.4 | 1.8
PB-GCS: 100%-0% | 44 | 44 | 48
NB-GCS: 100%-0% | 53 | 55 | 56
PB-GCS: 80%-20% | 49 | 51 | 56
NB-GCS: 80%-20% | 60 | 61 | 64
#sensors = 150
The influence of the grid side length on the number of chargers.
The smaller, the better. But the computation is also larger.

## Slide 68: Part II: Short Summary
Our contribution:
Propose two near-optimal algorithms to minimize the number of chargers: NB-GCS & PB-GCS.
Comparisons:
 | NB-GCS | PB-GCS
Performance | Good | Better
Time Complexity |  | 
 | NB-GCS | PB-GCS
Performance | Good | Better
Time Complexity |  | 

## Slide 69: Future Work
Allow the deployment of chargers at any place
Consider the obstacles between chargers and harvesters
Design duty-cycle scheduling schemes for chargers to save energy
Use novel heuristic or metaheuristic algorithms to solve the problem

## Slide 70
Thank you!