## Slide 1: Wireless Broadcasting with Optimized Transmission Efficiency
Jehn-Ruey Jiang and Yung-Liang Lai
National Central University, Taiwan

## Slide 2: Wireless Broadcasting
Broadcasting is one of the most fundament operations in wireless networks
Each node has one antenna of which wireless transmission range is modeled as a circle of fixed radius R
One node, called the source node, would like to disseminate a packet to all network nodes
Nodes receiving the packet will intelligently decide whether to rebroadcast it or not
R

## Slide 3
Totally redundant
retransmission
Retransmission of some extra coverage

## Slide 4: A Simple Scheme -- Flooding
Flooding is a simple method to realize broadcasting
But it incurs a large number of redundant retransmissions
  leading to low transmission efficiency
  Resulting in the well-known “Broadcasting Storm Problem”

## Slide 5: Proposed Scheme
In this paper, an optimized broadcast protocol (OBP) is proposed
  to optimized the transmission efficiency of wireless broadcasting 0.55  0.61
  while maintaining as high as possible reachability  100%

## Slide 6: Outline
Transmission Efficiency of Broadcasting
  Related Work
  Optimal Flooding Protocol (OFP)
  Broadcast Protocol for Sensor networks (BPS)
  Hexagon Flooding Protocol (HFP)
Our solution
  Optimized Broadcasting Protocol (OBP)
Performance Analysis and Comparison
Conclusion

## Slide 7: Transmission efficiency of Broadcasting
Transmission efficiency(TE) is the ratio
  TE= Effective Area Covered / Total Transmission Area =|CA  CB|/ ( |CA|+|CB|)
For instance, Node A broadcasts one packet and then Node B rebroadcasts one packet,
  Effective area covered by A and B is |CA  CB|
  Total Communication Area is | CA | + | CB |
Node A Node B
Node A Node B
|CA |
|CB |

## Slide 8: Transmission efficiency : Upper bound
Transmission efficiency(TE) is the ratio
  TE= Effective Area Covered / Total Transmission Area =|CA  CB|/ ( |CA|+|CB|)
When Distance between A and B = Transmission radius R  TE reaches the theoretical upper bound 0.61
Node B
Node A
R

## Slide 9: Existing Broadcasting Protocol :OFP
Geometry-based protocols
  Assume that each node is aware of its own location to make retransmission decisions
Optimal Flooding Protocol (OFP)
  With the highest transmission efficiency among all existed Geometry-based protocols, so far
  Proposed by Paruchuri et al., in IEEE WCNC 2002
  Has transmission efficiency of 0.41
  About 67% of the theoretical upper bound

## Slide 10: Optimal Flooding Protocol (OFP)
Idea
  based on a regular hexagonal partition of the network
  only the nodes nearest to hexagon vertexes need to rebroadcast
s
S: Source node, the node to broadcast a packet throughout the network
Do nothing
The nearest one has to rebroadcast
R

## Slide 11: Optimal Flooding Protocol (OFP)
Steps
s
s
s
s
Step.1
Step.2
Step.3
(1)
(6)
(6)

## Slide 12: Optimal Flooding Protocol (OFP)
Steps
Step.4
s
(12)
Total Retransmission times =(1)+(6)+(6)+(12)= ( 25 ) times
Result: Network Area is covered so every node receive the packet
s

## Slide 13: Can we further improve the transmission efficiency?
Transmission
Efficiency
?
OFP, 0.41
Upper Bound 0.61

## Slide 14: Our proposed protocol: OBP
Basic Idea of OBP (Optimized Broadcast Protocol)
  To activate nodes to rebroadcast Ring by Ring
    Nodes on centers of hexagons
    Nodes on vertexes of hexagons
s
s
s
s
Step.1 (1)
Step.2 (3)
Step.3 (6)
Total Retransmission times of OBP =(1)+(3)+(6)= ( 10 ) times
25 (OFP) vs 10 (OBP)

## Slide 15: OBP : Activation Sequence
C0,0
C0,0
V1,0
V1,1
V1,2
C0,0
V1,0
V1,1
V1,2
C1,0
C1,1
C1,2
C1,3
C1,4
1.node S broadcasts a packet
2. To activate three vertexes node {V1,0, V1,1, V1,2}
3. Each Vertex Node activates Two Center Nodes
C1,5
C0,0
V1,1
V1,2
C1,0
C1,1
C1,2
C1,3
C1,4
C1,5
V2,0
V2,1
V2,2
V2,3
V2,4
V2,5
4. Each Center Node activates One Vertex Node
… Finally, all centers of hexagons will activated to rebroadcast

## Slide 16: OBP : Basic Structure
By the way, all centers of hexagons will activated to rebroadcast ring by ring
side
length (R)
C2,6
S
C1,2
C1,1
C1,0
C1,4
C2,5
C2,4
C1,3
C2,3
C2,2
C2,1
C2,11
C2,10
C2,8
C2,9
C2,7
V1,0
V2,2
V2,1
C1,5
V2,4
V2,5
V1,1
V1,2
C0,0
C2,0
V2,0
V2,3
Horizontal axis
C3,0
C3,1
C3,2
C3,3
C3,4
C3,5
C3,6
C3,7
C3,8
C3,9
C3,10
C3,11
C3,12
C3,13
C3,14
C3,15
C3,16
C3,17
V3,0
V3,1
V3,2
V3,3
V3,4
V3,5
V3,6
V3,7
V3,8
In each ring, index started
along the Horizontal axis
Ring 1
Ring 2
Ring 3

## Slide 17: OBP: Two Key Components
Two key components of OBP
  How to calculate location of Ci,j
    Position of {Ck, i} = Geometric Mapping G(Ck,i)
s
G(C1,0)
C1,0
s
Ck,i
Ck+1,w
Ck+1,w+1
  How to find two next-level neighboring center nodes Ck+1,w Ck+1,w+1 of Ck,i
    Activation Target Mapping T(Ck,i)

## Slide 18: Geometric Mapping
.

## Slide 19: Activation Target Mapping
.
C2,6
C1,2
C1,1
C1,0
C1,4
C2,5
C1,3
C2,3
C2,11
C2,10
C2,9
C2,7
C1,5
C0,0
C2,0
C3,0
C3,1
C3,2
C3,3
C3,4
C3,5
C3,6
C3,7
C3,8
C3,11
C3,12
C3,13
C3,14
C3,15
C3,16
C3,17
Sector 0
Sector 1
Sector 2
Sector 3
Sector 4
Sector 5
A0
A3
A4
A5
C3,10
C3,9
C2,8
C2,2
C2,1
S
C2,4

## Slide 20: OBP : Algorithm
The step for the source node S to broadcast a packet P:
  S1. S sends the packet P(LS, F) with F={LV1,0, LV1,1, LV1,2}.
C0,0
V1,0
V1,1
V1,2
For example, LV1,0 is used to indicate the location of vertex node V1,0
for the node which is nearest to this location to be activated

## Slide 21: OBP : Algorithm
For other node Y receiving P(LS, F)
  S1. If Y is not closest to the target locations, Y stops
  S2. If Y is a vertex node, it will activate two center nodes
  S3. If Y is a center node, it will activate one vertex node (when required)
V1,0
V1,1
V1,2
V2,0
C1,0
C1,1
C1,0
Each vertex(or center) node can know whether it is nearest the location by
exchange location information (like HELLO message) in the network initial stage

## Slide 22: OBP : Details
The step for the source node S to broadcast a packet P:
  S1. S sends the packet P(LS, F) with F={LV1,0, LV1,1, LV1,2}.
Steps for other node Y receiving P(LS, F):
  S1. If Y receives P for the first time, it registers P. Otherwise, it drops P and stops
  S2. If Y is not a node nearest to a location in F, it stops
  S3. If Y is nearest to a center node associated with Ck,i of a location in F and T(Ck,i), then Y sends P(LS, F) and stops, where F={LVk,i} if T(Ck,i) and F= if T(Ck,i)= .
  S4. If Y is nearest to a vertex node associated with Vk,i of a location in F, X sends P(LS, F) and stops. Indeed, Y can calculate T(Ck1,i)= {Ck,w, Ck,w+1} based on indexes k, i and then set F={LCk,w, LCk,w+1}
    Based on Geometric Mapping G(Ck,i), Activation Target Mapping T(Ck,i) , OBP can be designed to broadcast packet into the network

## Slide 23: Performance Analysis of OBP
Transmission efficiency η:
OBP approximates the theoretical upper bound of transmission efficiency by a ratio of ηOBP/ηU  90%

## Slide 24: OBP is with higher transmission efficiency
Transmission
Efficiency
OFP, 0.41
Upper Bound 0.61
OFP, 0.55
In IEEE WCNC 2002
2009

## Slide 25: Performance Comparisons
Required Transmissions for OBP and OFP
Chart: Level of Hexagon Rings
| 2 | 3 | 4 | 5
OBP | 10 | 28 | 55 | 91
OFP | 25 | 55 | 97 | 151

## Slide 26: Reachability of OFP and OBP for various node densities
We also observe OBP may not have 100% reachability when the node density is not sufficiently high
Chart: Densitity
| 10 | 12 | 14 | 16 | 18 | 20
OBP | 0.95 | 0.98 | 0.98 | 0.99 | 0.99 | 0.99
OFP | 1 | 1 | 1 | 1 | 1 | 1

## Slide 27: Conclusion
We have proposed an optimized broadcast protocol (OBP) for wireless networks
The Key idea of OBP is to select nodes based on a hexagon ring pattern to minimize the number of retransmissions for better transmission efficiency
Analysis result shows that OBP’s transmission efficiency is over 90% of the theoretical upper bound
Currently, we are studying broadcasting in 3D wireless network
Thanks for your listening